AUSTRIA EMAIL HIGH-PERFORMANCE UPRIGHT HEAT EXCHANGER TANK

Internal steel boiler enamelled according to DIN 4753 with rod anode

Particularly large-surface heat exchangers

High-quality thermal PU foam insulation

Internal boiler foamed directly to the outer cladding

Silver-grey foil jacket delivered separately (ordered separately)

Ø 180 mm flange for combination with a built-in electric heater or a built-in finned tube heat exchanger and a high-performance pipe array pulled into the base, sealed into the boiler and enamelled for optimal heating of tank content

Dummy flange and Ø 180 mm ISO cover hood attached

2 sensor channels installed for pipe array control

Thermometer attached, 1 ATR can be mounted

Nominal capacity:						500 l

Operating pressure, boiler:				max. 10 bar

Operating pressure, tube register:			max. 10 bar

Operating temperature, boiler:				max. 95°C

Operating temperature, heat exchanger:		max. 110°C

Water connections:						1“ AG

Heating connections:					1“ IG

Circulation connection:					1“ AG

Dimensions incl. Insulation (HxW/D)			1838 x Ø 750 mm

Diagonal height:						1970 mm

Flange diameter/installation depth:			Ø 180/580 mm

Heating surface:						4,0 m²

Weight including packaging:				180 kg

Standby energy consumption according to

EN 12897, less than or equal to:				2,7 kWh / 24 h

Make:				 Austria Email

Model: 				HR 500

Art.Nr.: A 245 28

Stand 24.11.2011			*Subject to technical changes and printing errors